Vacuum filter ZF-50L

Working principle Please make sure that the stainless steel funnel of this equipment should be equipped with different filter materials (filter cloth, filter screen, filter membrane, etc., which needs to be prepared by the customer) before usage. Put the materials which need to be filtered on the filter layer evenly, and then connect the glass filter flask with a vacuum pump. The material in the funnel can be filtered according to negative pressure principle. And then the material after filtration is pumped into glass filter flask. The standard of the filtered material depends on the specifications of the filter cloth used. This equipment can be used for solid-liquid separation, material drying, liquid decontamination and other operations.

Basic configuration • The glass filter flask uses high borosilicate glass (expansion coefficient 3.3), which has stable performance. • 304 stainless steel funnel, with ₵ 4mm hole at the bottom of the funnel. • Using aluminum alloy + stainless steel material as frame. • Glass material discharging valve. • There is a universal wheel with brake at the bottom of the equipment, which can be moved as a whole and be operated conveniently.

Technical parameters

| Model | ZF-50L |
| --- | --- |
| Volume of glass filter flask | 50L spherical shape |
| Vacuum | 0.098Mpa |
| Filter flask Φ470m 3 ports | Funnel connection port | Φ80mm flange port |
|  | Vacuum port | 24# standard port |
|  | Material discharging port | Φ45mm flange port |
| Vacuum valve | 24# vacuum valve; vacuum nozzle (pagoda joint) with 12mm outer diameter |
| Material discharging port | Φ45 spherical convex port (glass + PTFE core C type valve), material discharge valve ₵20mm |
| Funnel dimension | Φ450×250H(mm) about 39L |
| Overall dimension(W*D*H) | 580(W)×600(D)×1530(H)mm |
| Net weight | 38KG |
| Packing dimension | 1470×620×700mm wooden package 0.64m³ |
| Packing weight | 67KG |

Picture

Vacuum suction filter is produced according to the needs of the general biological/pharmaceutical development industry and is based on the existing single-layer glass reaction kettle to improve development of derivative products, mainly used for liquid-liquid extraction and other normal temperature reactions.

Product Features:

- The suction filter bottle is made of GG17 high borosilicate glass material, which contains properties designed to withstand general chemical reactions and temperature changes.

- Stainless steel buchner funnel provides durability and ease of sanitation.

- Special PTFE material mixing plug designed for high corrosion resistance.

- Discharge outlet made of glass and PTFE valve flange mouth with a spherical arc shape interior allowing for easier solid material removal.

- Sealing performance metrics reach 0.095 MPa under stationary vacuum state.

- The structure and design of this unit allows for easy mobility with innovative and practical use applications.